## Slide 1: TPC Cost Estimates
EIC Tracking TPC Meeting, BNL
Feb 06, 2014
Ron Soltz, LLNL

## Slide 2: Estimation Methods
Bottom-up detailed estimate
Top down scale from other projects
Start with 2. but plan a path to get to 1.

## Slide 3: Two well known TPCs and design cost estimates
STAR CDR (1992)
  https://drupal.star.bnl.gov/STAR/files/StarCDR.pdf (Table 9-2)
ALICE TDR (2003, CHF=$0.82)
  http://cds.cern.ch/record/451098?ln=en
Item | Cost ($k)
TPC Mech. Design | 1400
TPC Mech. Fab. | 5300
TPC Elec. Design | 750
TPC Elec. Fab. | 2300
Total | 9750
Electronics costs = 1/3 total for STAR, ½ total for ALICE (more with readout)
  scale by channel count
Mechanical + HV = remainder
  scaling less obvious: volume, surface, ?

## Slide 4: Electronics scaling estimate
Channel count driven by dE/dx and Dp/p requirements
  for dE/dx assume of order n=50 pad rows
    needed to sample long tails of Landau dist.
    OK to +/- 20%, pending easy simulation study
  for Dp/p, ePHENIX LOI requires 1% at 10 GeV
    assume 5% for now, same as STAR estimate
    additional improvement from Si vertex layers?
    Dp/p ~ (p sf) / (B d2 √n) [see next slide]
    sfSTAR = 4e-3 angular pad width (includes √12 factor)
    sfEIC = sfSTAR * (1.5T/.5T) * (0.65m/2m)2 * (50/45)1/2 = 1.3e-3
    50*2pi/1.3e-3 = 240k channels per side
    note 1.3e-3 * 150mm = 0.2mm pad width at 150 mm

## Slide 5: STAR CDR momentum resolution formula
tracking down note to check assumptions

## Slide 6: Simple scaling cost estimates (base on STAR)
Electronics
  Last upgrade $16/channel * 240k = $3.8M (per side)
  Next upgrade $5/channel * 240k = $1.2M (per side)
Mechanical = $6.7M
  scale by Volume: $6.7M * ( 0.652 * 2 m3 ) / (22*4 m3) = $0.33M (don’t believe this one)
  scale by Surface $6.7M * (0.65 * 2 m2) / (2*4 m2) = $1.1M
  scale by Length $6.7 * 2m/4m = $3.4M
Discussion
  upper limit = $7.2M
  lower limit = $2.3M
  better estimates require real work

## Slide 7: Working towards improved estimates and design
Fixed Constraints
  Outer Radius = 90cm (80cm with DIRC)
  Inner Radius = 15cm (30cm with 4-layers Si)
  Length = 2m (|h|<1 coverage)
  B-field = 1.5 T
Main Drivers and dependencies
  Dp/p = 1% at 10 GeV
    angular resolution (pad width)
    radial depth (dimensions)
    drift diffusion (gas and E-field)
    distortion (E-field, gain, ion feedback)
  dE/dx (PID to 1 GeV plus some discrimination in relativistic rise)
    gas and signal gain
    pad width and depth
    radial depth

## Slide 8: Initial design studies
Simulation
Dp/p for TPC (w/ Si layers)
dE/dx vs. channel count
E-field shaping
Radiation length
Tracking efficiency
Laboratory
Gas drift and diffusion
Gain and ion backflow
Electronics testing
Field cage resilience

## Slide 9: Collaboration issues
Dedicated TPC wiki page needs to be created/maintained
Do we have mechanism for archiving notes?
Budgeting request
  Equipment for specific lab tests
  Prototype electronics (SAMPA) for testing
  Preliminary engineering drawings